## Slide 1: Pipelined basic instruction set simulation
Wei Hong and Tengyu Sun

## Slide 2: Architecture
Current stage

## Slide 3: Implementation
5 stages
IF -> ID -> EX -> MEM -> WB
Pipeline
represented as an instruction array of size 5. The instruction objects are passed around the 5 stages
Registers
  16 general purpose registers
  16 floating point registers
  16 vector registers
  One program counter
Instruction state

## Slide 4: Full ISA support
Data transfer
  lb, lbu,sb, lw, sw, lsp, witf, wfti
Arithmetic and logical
  add,sub, addi, subi, mul, muh, mulu, muhu, div, divu, modu, and, or, not, xor
  Rr, srl, sra, sl, slt, sltu, slti, sltiu
Control
  J, jal, beq,bgez,blez, bltz, break
Floating point
addsp, subsp, mulsp, divsp, sltsp
Cache
pref
SIMD
move, copys, copyu, insert, fillb, vaddb, vsubb, vmulb, vdivb
vmodb, ceqb, cleb, cleub, cltb, cltub

## Slide 5: Assembler implemenation
2-pass
First pass: load labels into a Map<label, line_number>
Skip blank lines / comments
Second pass:
Take assembly language clauses, parse them into binary instruction.
If labels are encountered, offset is calculated according to the its their line numbers.

## Slide 6: Demo 1
preload mem[100] = 1, mem[101]=2
lb $0,$1,100 #$1 = 1
lb $0,$2,101 #$2 = 2
add $1,$2,$3 #$3 = $1 + $2 = 3
bgez $3,L1 #$3>0, branch to sb…
lb $0,$3,100
L1: sb $0,$3,102 #mem[102] = 3
break
preload mem[100] = 1, mem[101]=2
lb $0,$1,100 #$1 = 1
lb $0,$2,101 #$2 = 2
sub $1,$2,$3 #$3 = $1 - $2 = -1
bgez $3,L1 #$3<0
lb $0,$3,100
L1: sb $0,$3,102 #mem[102] = 1
break
Demo 2